## Slide 1
BIM for Digital Twin: the case study of Trento
Silvia Ricciuti¹, Oscar Roman², Elisa Farella², Andrea Gobbi³, Diego Viesi¹, Fabio Remondino²
¹ FBK - Center for Sustainable Energy (SE)
²FBK - Center of 3D Optical Metrology
Fondazione Bruno Kessler (3DOM)
³FBK – Center of data Science for Industry and Physics (DSIP)
sricciuti@fbk.eu www.fbk.eu

## Slide 2: Agenda InCUBE
Project description
Activity description
Process of the activity
Results
Conclusion

## Slide 3: EU project InCUBE - An INClUsive toolBox for accElerating and smartening deep renovation
InCUBE is a Horizon project in the field of Efficient, sustainable and inclusive energy use.
Keywords: off-site manufacturing, digital twins, digital logbook, robotic systems, smart readiness, lean construction, upskilling workforce, social inclusiveness, user comfort, renewable energy communities.
The project duration is from July 2022 (M1) to June 2027 (M60). From July 2026 to June 2027 there should be the one monitoring year.
Partners:

## Slide 4: EU project InCUBE
WP1 : Foundations for Smartening and Accelerating Deep Renovations: InCUBE framework
WP2 : InCUBE Technological Pool of Solutions (Hardware-Driven Innovation)
WP3 : A digital-twin enabled Unified Design/ Construction/ Renovation process
WP4 : Enhanced evaluation and optimised renovation planning and retrofitting: Using Digital Twins for Data- driven decision making
WP5 : Reduced Performance Gap and Value Chain Interoperable Integration
WP6 : Upskilling and Gender Mainstreaming workforce
WP7: Transformation of Deep Renovation: InCUBE Demonstration, Evaluation and Impact Assessment
WP8 : Business Models and Roadmap to Innovation & Collaboration
WP9 : InCUBE Communication, Dissemination and Exploitation
WP10: Project Coordination and Management
Before of the Italian demo – After of the Italian demo
InCUBE demos buildings – Trento , Zaragoza, Groningen
Some technologies applied in the demos

## Slide 5: The InCUBE Trento demo site
Santa Chiara district (B1, B2, B3, B4, B5, B6) – Total floor area: 24368 m2 including gym e auditorium
Historical building B6
Floor area: historical part 5400 m2 and Palabocchi gym and Auditorium that are respectively 1080 m2 and 1458 m2.
Construction date: 1235 (1980)
Occupants/users: more than 1500 people
Energy Needs: 214 kWh/m²/y  188 kWh/m²/y
Current RES production: 56 MWh/y  339 MWh/y
EPC Class: D  B
Current SRI: 14.2% 85.7%

## Slide 6: Context Building renovation
Building Renovation
Improve Energy Efficiency
Retrofit of outdated systems
Enhancing thermal insulation
Integrate renewable energy sources
Digital Twins
Digital replicas
Geometric Digital Twin (GDT)
Data integration layer
(real-time or historical data)
Simulations
Indoor conditions & Technological Systems
HVAC installation
Automated energy management
Energy-efficient lighting

## Slide 7: Current workflows for digital twins General common workflows
3D surveying (Photogrammetry, LiDAR, drone, etc.)
3D geometric model, Building Information Model (BIM)
Building Energy Model (BEM)
Energy Digital Twin
3D reconstruction, Scan-to-BIM, meshing, semantic enrichment
Enrichment with energy components (static information)
Enrichment with dynamic data and analytics
Link to the real world object
Boundary representation (B-Rep) models for simulations

## Slide 8: Current workflow Energy analysis from 3D point clouds
SCAN-TO-BIM
BIM / DT SOFTWARE
ENERGY ANALYSIS
UNSTRUCTURED POINT CLOUD
RESULTS
Many processing steps/Software (mostly commercial) – Compatibility issues/frequent loss of data

## Slide 9: The InCUBE Trento demo site
(1) 3D modelling of the general building envelope with aerial data

## Slide 10: The InCUBE Trento demo site
(2) 3D surveying/TLS (Leica RTC360) / façades and indoor (about 360 scans) B6 block

## Slide 11: InCUBE 3D reality-based surveying and 3D modelling
Current regulations impose some flight restrictions in urban areas for safety reasons. To generate the BIM models instead of UAV/drones there was the need to use terrestrial laser scanning (TLS) techniques.

## Slide 12: The InCUBE Trento demo site
(3) Cleaning and resample of point clouds

## Slide 13: The InCUBE Trento demo site
(4) Data fusion/ multi-resolution and complete 3D final point cloud

## Slide 14: The InCUBE Trento demo site
(5) Geometrical BIM model

## Slide 15: BIM to BEM Workflow
https://github.com/3DOM-FBK/InCUBE
TLS dataset
BIM model

## Slide 16: BIM to BEM Workflow
Zone_A2
Zone_A1
IoT EDGE COMPUTER
SMART PLUGS
MULTISENSORS
Zone A1 - sensor_01
Zone A2 - sensor_02
sensor_01
sensor_02

## Slide 17: BIM to BEM Visualization and predictive models
Z-sensors energy consumpition data are visualized in a dedicated dashboard
Foundational time series forecasting models are trained (few shot with different % of historical data) for predicting the next 24 hours of energy demand

## Slide 18: BIM to BEM Workflow
Zone_A2
Zone_A1
IoT EDGE COMPUTER
SMART PLUGS
MULTISENSORS
Zone A1 - sensor_01
Zone A2 - sensor_02
6-months temperature data

## Slide 19: BIM to BEM Workflow
SENSOR PLACEMENT AREAS
CFD SIMULATIONS AND ANALYSIS
REAL TIME DATA AND MODEL VALIDATION
3
3A
RESULTS
5
6
WALL MASKS
EXTRACTION
4
UNSTRUCTURED POINT CLOUD
ENERGY-RELATED INFORMATION (.JSON)
2C
INFORMATIONAL LOAD DICTIONARIES
(ILD)
2D
CLASSIFIED POINT CLOUD
TOPOLOGIC MODEL (TBIM)
2B
GEOMETRIC DIGITAL TWIN (gDT)
2A
1A
t = ti+ t(i + 1)
GEOMETRIC RECONSTRUCTION PROCESS
ENERGY ANALYSIS

## Slide 20: BIM to BEM Workflow
3. Model for simulations
1. geometric DT
Classified point cloud
2. Topologic (TDM)
[Roman, O., Mazzacca, G., Farella, E. M., Remondino, F., Bassier, M., and Agugiaro, G.: Towards Automated BIM and BEM Model Generation using a B-Rep-based Method with Topological Map, ISPRS Ann. Photogramm. Remote Sens. Spatial Inf. Sci., X-4-2024, 287–294.]
1
2
3

## Slide 21: BIM to BEM Workflow
3. Model for simulations
1. geometric DT
Classified point cloud
2. Topologic (TDM)
Floorplan extraction

## Slide 22: BIM to BEM Workflow
3. Model for simulations
1. geometric DT
Classified point cloud
2. Topologic (TDM)
ENERGY MODEL
Class_id
Area
U-value
Internal\External walls
TBIM - VOLUMETRIC MODEL
Volume
Room Type
# Thermal zone
Temperature setpoints
Orientation
# devices inside

## Slide 23: Digital twin From BIM to BEM
InCUBE Conceptual architecture

## Slide 24: Digital twin From BIM to BEM
Taki it and transform in json format and trasform it a data model – we pick most relevant information surface/year/material and level of details
Sensinac iot platform
Eclipse foundation and it is open
Data model that rapresent this data – simple but effective
Sensors in general
Transfor model in senac rapresentation through digital twin

## Slide 25: BIM to BEM Workflow
Developments on the back-end
  Improved file handling methods and revised the file paths to consider the site name and the different document categories
  Added integration of the DBL with BIM IFC files of the buildings
    BIM IFC format  CSV format  JSON format
    Covered aspects: Building, Storey, Space
    New webservice getBIMinfo: /getBIMinfo?site=ITDEMO&aspect=building

## Slide 26: BIM to BEM Workflow
Development of the web-based UI
Login page

## Slide 27: BIM to BEM Workflow
‘Dashboard’ section

## Slide 28: BIM to BEM Workflow
‘Monitoring’ data section

## Slide 29: BIM to BEM Workflow
Documents section
  Organised by document types
  Sorting by column
  Search box

## Slide 30: BIM to BEM Workflow
Management section

## Slide 31: InCUBE Digital twins
Digital Twin – Integration Activities
  S-BEMS for real-time data
  Integration of historical data (statistics) and KPIs
  Logbook for BIM and BIM2BEM data

## Slide 32: InCUBE Digital twins
Digital Twin – User Interface
  Customizable interface for each demo site
  2D representation of products
  3D representation of buildings

## Slide 33
thank you.